## Slide 1: CPU vs GPU Data Processing
PARALLEL COMPUTING MINI-PROJECT | LAB EVALUATION
2D Convolution using OpenMP and CUDA
Team 7 | Guide: Srushti Gani
CPU
OpenMP threads
GPU
CUDA thread blocks
vs
Name | USN
Nupur Bagave | 01FE24BCI029
Vedant Khot | 01FE24BCI028
Parth Karpe | 01FE24BCI062
Hrishikesh Patil | 01FE24BCI043

## Slide 2: Problem Statement and Objectives
THE PROBLEM
Run the same numerical operation on CPU threads (OpenMP) and on the GPU (CUDA), then compare performance
1
Parallelize a nested-loop numerical workload on a multicore CPU
2
Map one output element to one CUDA thread
3
Measure CPU time, CUDA kernel time and GPU end-to-end time
4
Study effect of matrix size and thread count on time, speedup, efficiency
5
Verify CPU and GPU outputs element by element
Notes: State the team topic and the five objectives.

## Slide 3: Workload: 2D Convolution (3 × 3 Kernel)
B[i][j] = Σ Σ A[i+r][j+c] × K[r][c]
for r, c = 0..2 | valid convolution, no padding, stride 1: output is (N−2) × (N−2)
Kernel [1 0 −1] on every row; 9 multiply-adds per output element
Input: mt19937, seed 42, uniform [0,1), float, identical for CPU and GPU
3 × 3 KERNEL
1
0
−1
1
0
−1
1
0
−1
Input | Output | Role
1024 × 1024 | 1022 × 1022 | Small / scaling
2048 × 2048 | 2046 × 2046 | Medium / scaling
4096 × 4096 | 4094 × 4094 | Large / final validation

## Slide 4: Sequential Algorithm
1
Generate input with fixed seed; initialize 3 × 3 kernel
2
Compute output dimensions (N−K+1) × (N−K+1)
3
For each output (i, j): sum = 0
4
For r, c in 0..2: sum += A[i+r][j+c] × K[r][c]
5
Store sum in
B[i][j]
Each output element depends only on its input window, so all outputs are independent and ideal for parallelism.

## Slide 5: Parallel Design: OpenMP (CPU)
C++ / OPENMP
#pragma omp parallel for collapse(2)
for (int i = 0; i < outRows; ++i)
for (int j = 0; j < outCols; ++j) {
float sum = 0.0f;
for (int r = 0; r < 3; ++r)
for (int c = 0; c < 3; ++c)
sum += in[(i+r)*N + (j+c)]
* k[r*3 + c];
out[i*outCols + j] = sum;
}
collapse(2) merges both loops into one iteration space
Shared host memory: no data transfer
Thread counts tested
1
2
4
8
16

## Slide 6: Parallel Design: CUDA (GPU)
16 × 16
256 threads per block
256 × 256
blocks for a 4096² grid
sm_86
target architecture
One thread computes one output element
x = blockIdx.x·blockDim.x + threadIdx.x (same for y); guard: x < N−2 && y < N−2
Kernel time
GPU computation only
End-to-end time
host→device copy + kernel + device→host copy
Comparing kernel time with end-to-end time is the key idea of this experiment.

## Slide 7: OpenMP vs CUDA
Aspect | OpenMP | CUDA
Hardware | Multicore CPU | NVIDIA GPU
Parallel unit | CPU threads | GPU threads
Memory | Shared host memory | GPU global + host memory
Style | Directives + runtime | Kernel + grid/block/thread
Variable | 1, 2, 4, 8, 16 threads | 16 × 16 blocks
Main overhead | Scheduling, memory bandwidth | Kernel launch, host-device transfers

## Slide 8: Experimental Setup and Methodology
PLATFORM
Windows 11, i5-13450HX, 16 GB RAM, RTX 3050 6GB (driver 581.95)
TOOLCHAIN
CUDA Toolkit 13.4 (nvcc 13.4.92), MSVC 19.51, arch sm_86
BUILD
RUN
cl /O2 /openmp
nvcc -O3 -arch=sm_86 -Xcompiler="/openmp"
convolution_experiment.exe <size> <threads>
15 runs
3 sizes × 5 thread counts
METRICS
Speedup = T(1) / T(p)
Efficiency = Speedup / p × 100

## Slide 9: Correctness Verification
0
Max error
0
Mean error
0
Mismatches
PASS
Status
✓
Every CPU output element compared with the GPU output; tolerance |diff| ≤ 1e-5
✓
First 10 output values also identical in both program outputs
Result holds for all 15 recorded runs and the 3 validation runs.

## Slide 10: Results: CPU Scaling (4096 × 4096)
Threads | Time (ms) | Speedup | Efficiency
1 | 42.02 | 1.00 | 100%
2 | 20.81 | 2.02 | 100.9%
4 | 10.76 | 3.91 | 97.6%
8 | 10.21 | 4.11 | 51.4%
16 | 8.44 | 4.98 | 31.1%
Chart: OpenMP time vs threads (ms)
| 1 | 2 | 4 | 8 | 16
CPU time (ms) | 42.02 | 20.81 | 10.76 | 10.21 | 8.44
Near-linear up to 4 threads, then diminishing returns.

## Slide 11: CPU Efficiency vs Thread Count
Chart: Efficiency (%)
| 1 | 2 | 4 | 8 | 16
1024² | 100 | 83.6 | 75.6 | 61 | 32.8
2048² | 100 | 105.4 | 77.7 | 48.4 | 30.3
4096² | 100 | 100.9 | 97.6 | 51.4 | 31.1
Falls from ~98% (4 threads) to ~31% (16 threads) at 4096²
Causes: memory bandwidth, scheduling overhead, cache behavior
Small 1024² input cannot keep many threads busy
Values above 100% are timing noise (frequency, scheduling), not true super-linear scaling

## Slide 12: Results: GPU Kernel vs End-to-End
3.96×
Kernel is faster than 1-thread CPU at 4096²
0.15–0.82×
End-to-end speedup is below 1×: transfers cost more than the compute saved
9
multiply-adds per element: low compute per byte moved
Chart: Time (ms), original sweep
| 1024² | 2048² | 4096²
CUDA kernel | 0.55 | 2.19 | 8.75
GPU end-to-end | 3.64 | 13.85 | 50.61
CPU 16 threads | 0.54 | 2.35 | 8.44

## Slide 13: Final Validated Run: 4096² with 16 Threads
Run | CPU ms | Kernel ms | End-to-end ms | Kernel speedup
1 | 7.083 | 0.977 | 16.458 | 7.25×
2 | 7.193 | 0.978 | 16.644 | 7.36×
3 | 7.146 | 0.977 | 17.747 | 7.31×
Average | 7.141 | 0.977 | 16.949 | 7.31×
NOTE ON THE EARLIER SWEEP
The earlier sweep showed ≈ 8.75 ms kernel time for this configuration; the repeated controlled run is reported as the validated result (probable cause: GPU warm-up / power state, not isolated)
≈ 7.31×
kernel speedup
≈ 0.42×
end-to-end speedup
All runs PASS

## Slide 14: Key Observations and Discussion
1
OpenMP scales well to 4 threads; efficiency drops beyond that
2
CUDA kernel is up to ~7.3× faster than 16-thread CPU compute (validated run)
3
Data transfer dominates GPU end-to-end time for this low-arithmetic workload
4
GPU pays off when data stays on the device across many operations or compute per byte is higher
5
Larger matrices give more parallel work but also more data to move

## Slide 15: Conclusion and Repository
1
CPU and GPU results match exactly (0 mismatches in all runs)
2
CPU: ~5× speedup at 16 threads; GPU: ~7.3× kernel speedup but ~0.42× end-to-end
3
Lesson: always report kernel time and end-to-end time separately
4
Future work: shared-memory tiling, pinned memory, streams to overlap transfers, batched images
~5×
CPU speedup, 16 threads
~7.3×
GPU kernel speedup
~0.42×
GPU end-to-end speedup
Thank you. Questions?